## Slide 1: Hardware: Lights, Cables & Mics
Objective: 2.02

## Slide 2: Lighting

## Slide 3: Common Lighting Issues
Think back to when we talked about aperture earlier. These issues I have seen too many times in House Hunters and other professionally shot shows. The iris controls the aperture which lets in the appropriate amount of lighting

## Slide 4: Advanced Lighting Terms
We call the typical lighting setup for filming and interviews, 3-point lighting. The 3-point lighting setup is made up of the Key Light, Fill Light and Back Light.

## Slide 5: Advanced Lighting Terms
  The main source of light for the video production; pointed at the set to illuminate the subject(s). This is the first light you set up
Key Light
  Less intense light used to eliminate or soften the shadows. Should be set up 90 degrees from the Key Light (other side of subject). Move farther away from subject to make it less intense.
Fill Light
  Illuminates the subject(s) from behind; separates the subject(s) from the background itself. Creates a more dynamic image, set up last
Back Light

## Slide 6
Just Key Lights
Key Light and Fill Lights
Three Point Lighting Setups

## Slide 7: Do you think cartoons and stop motion films use 3 point lighting?
True
False
Notes: True or False
Use this template to do a quick check of students’ perceptions during your lesson.
🍐 This is a Pear Deck Multiple Choice Slide. Your current options are: A: True, B: False,
🍐 To edit the type of question or choices, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 8
Back light
Even animators have to think about how lighting a scene when they are creating it digitally.

## Slide 9
This is another name for Back Light
This would be the Key Light

## Slide 10: Gel - Lighting Equipment
Color gel is a transparent colored material that is used in theater, event production, photography, videography and cinematography to color light and for color correction

## Slide 11: Color Temperature
Color temperature describes the “color” of white light by a light source radiated by a perfect black body at a given temperature measured in degrees Kelvin.
Meaning???
Light can be warm (yellow/orange) or cool (blue). Color temperature can even affect the tone of your story.

## Slide 13: The next slide is a few shots from House Hunters. I show the original shot and then how I fixed it in the color correcting process
These issues stem from NOT white balancing or setting up proper lighting.

## Slide 15: Reflector - Lighting Equipment
A photography light reflector bounces existing light. And re-directs it back onto the subject. Reflectors are excellent tools for adding fill light.

## Slide 16: Umbrella - Lighting Equipment
Umbrellas produce indirect, bounced light; which produce a broader type of diffused lighting. Point an umbrella at a subject and voilà, you've got soft lighting!

## Slide 17: Cables:

## Slide 18: Composite (RCA) Cable
Common video & audio cable used by both consumers and professionals
Used for VCRs, DVD players, etc.
Color coded to distinguish between audio/video

## Slide 19: Component (RGB) Cable
Red, Blue, and Green color coded connectors
Carries high-def video signals only
Splits video signals into three parts for better detail and color accuracy

## Slide 20: Coaxial (F) Cable
Commonly used to transmit video signal (cable TV, antenna)
Can span long distances without signal loss
Carries audio and video

## Slide 21: BNC Cable
Used in professional settings
Connects video camera to switcher (mixer)
Two-pin locking system to prevent it from being unplugged

## Slide 22: Firewire Cable
Has high transfer speed - used with computers
Captures audio or video from recording device into the computer
Different looks depending on age
      4-pin
      6-pin (400)
      9-pin (800)

## Slide 23: HDMI Cable
High-definition
Carries digital audio and video
Combines audio and video signals into one cable to simplify connection

## Slide 24: Microphones

## Slide 26: 3 main Microphones to remember
Handheld Mic
Lavalier Mic
Shotgun Mic

## Slide 27: On Board Mic
Almost all cameras have some form of an on board mic.

## Slide 28: Handheld Mic
Most used microphone
Designed to be held in the hand, but they can also be clipped onto a microphone stand.
Pick up sound directly from the mouth.
Can be wired or wireless
Wired mics are constricted to the length of the cord

## Slide 29: Hand Held Mic
Perfect for:
Interviews
Speeches
Musical performances
News reporting
This microphone is useful for talking between two people and pointing it directly at their mouth.

## Slide 30: Lavalier mic
Also known as :
  Lapel mic
  Lav mic
  Wireless mic
  Clip-on mic

## Slide 31: Lavalier mic
Perfect for:
  Shooting from long distances
  Interviews
  Tours
  News casters
  Anytime the mic needs to be hidden

## Slide 32: Lavalier Mic - Pros
Pinned to the subject’s outerwear
Conceal them so that viewers can’t see the mic
The smallest microphone
The only microphone someone does not have to hold
Only picks up sound from one direction

## Slide 33: Lavalier Mic - Downside
Even though it allows the actor to be handsfree, this microphone is pinned to clothes and has to be close to the person’s mouth. Hair and clothing articles can muffle or rustle against this microphone causing unwanted or bad sound.

## Slide 34: Shot Gun Mic
Perfect for:
  Dialogue
  Close-ups
  Movie scenes
Also known as Boom Mic

## Slide 35: Shot Gun Mic
Attached to the camera
If attached to a boom pole, becomes a boom mic
Has a narrow pick up pattern
Should be pointed directly at or close to the audio source

## Slide 37: Shotgun & Boom mics
Boom mics and Shotgun mics are used the most because they can be held just off screen and still allow for good quality of sound.
They are the only mics that aren’t in front of the camera
But we have to be careful not to have it fall into the camera’s view (seen at the beginning of previous video), this happens all the time and you may catch them in your tv shows you are watching.

## Slide 38: Room tone
You want to record 30 seconds of silence when filming because it allows you to place this audio under jumpcuts in the editing process. Allows us to smooth audio cuts or issues in editing.
You should always get 30 seconds before and after you film to use for editing
No room is ever completely silent. If you listen right now, your room probably has the humming of a light source or computer source. Or you can hear noises from outside your room.

## Slide 39: Audio to Enhance Video
  Using the actual sounds of the environment in which the video takes place.
  Typically used to make the video seem more realistic.
Natural Sound (AKA Nat Sound)
  Dialogue added to a video production to explain the visual scenario and give the audience more information about what is happening in the video.
Recorded Narration (Voiceover)